## Slide 1: Tree Safety Analysis
Tree Assessment Congress
Wroclaw
28.02.2019 - 01.03.2019
Is your tree safe?
for: Instytut Drzewa
TreeCalc

## Slide 2: Speaker Profile
Erk Brudi - TreeConsult since 1993
Landscape Gardener
Landscape Technician
Court Certified Expert Witness
MSc, Urban Forestry
Notes: Good afternoon. Before I introduce you to my topic today. I would like to give you some background information about myself and my company.
40 years ago I started my career as an apprentice in landscaping
After that I gathered working experience in Germany the US and Australia and went to school again.

## Slide 3: Company Profile
Measuring and Evaluation of Tree Safety

## Slide 4: Company Profile
Measuring and Evaluation of Tree Safety

## Slide 5: Company Profile
Tree Mechanics Research

## Slide 6: Company Profile
Tree Mechanics Research

## Slide 7: Company Profile
Forensic Expert Witnesses
Why Tree Failure?
Forseeability?

## Slide 8: Company Profile
Forensic Expert Witnesses
Why Tree Failure?
Forseeability?

## Slide 9
 = 0,4
 = 0,28
 = 0,20
 = 0,16
Wind speed
Gustiness
Wind Loading
Wind Velocity in the Boundary Layer

## Slide 10
Blow pipe effects
Ulmus americana Calgary, Al, CDN
Wind Effects in urban Areas
Wind Loading
Gustiness in Urban Areas
Notes: 10

## Slide 11
Crests of hills are obstacles in the wind flow.
In the luv and on top of hills wind velocities are increased.
Topography
Wind Loading
Notes: 11

## Slide 12
Protection from neighbouring Large Scale structures
Wind Loading

## Slide 13
Crown reaction during storm gusts
Birch
0.12
0.25
Oak
0.35
Horsechestnut
Wind Loading

## Slide 14: Stuttgart Strength Tables
kN/cm2
longitudinal
radial
tangential
Material Properties of Green Wood

## Slide 15: Limit of Elasticity in Beech
1.94 700 0,277
3.60 1400 0,257
4.40 1610 0,273
2.52 950 0,265
elastic limit in %
MOE
strength kN/cm2
average 0.26
standard deviation 0.02
prop. limit in %
# 156, Beech
85 years old
Material Properties of Green Wood

## Slide 16: Steady State Balance
Load bearing Geometry
Diameter 100 cm
Growth
0,5 cm
Decay 30 cm
Mres bend= D3 x P/32

## Slide 17: Relevance of Hollow Cylinders
load
neutral axis
peak stress levels
occur in a stem‘s marginal fibres
neutral axis
Load bearing Geometry
Notes: 17

## Slide 18: Modes of Failure
TreeCalc is designed to evaluate Breaking Failure only
Breaking failure
Stem / Limbs/Branches
Uprooting failure
Failure of root soil matrix

## Slide 19: ArboSafe GmbH
Desktop Software for Pulling Test Evaluation, including wind load analysis, EN 1991/4-1
Desktop Software for Tree Appraisal, Calculating Root Loss Area
Online Software for Tree Safety Analysis,
Calculating Stem Breaking Resistance
Software Forge for Tree Safety Analytics
Notes: Good afternoon. Arbosafe is a software forge in a small niche of the niche market tree consultancy.
Since 2007 we create software for tree safety analytics.
In 2007 we developped arbostat software that is designed to evaluate data obtained from tree pulling tests. Arbostat speaks German and English.
Root Calc was out next much small project. It is used mainly for tree appraisal and allows for calculating root loss areas.
And finally in 2013 we developped TreeCalc an pay-as you-use online software which is mz today’ s topic.

## Slide 20: What is TreeCalc?
TreeCalc recognizes good Practice of Statics
Online Software to evaluate the breaking safety of tree stems
Why using TreeCalc?
Systematic and methodologically correct evaluation of the
breaking safety of tree stems
On site tree safety assessment
Favourably verified in combination with stem tomography

## Slide 21: Who is using TreeCalc?
TreeCalc recognizes good Practice of Statics
More than 850 users world wide
Consultants
Arborists
Public sector environmental officers
Scientists

## Slide 22: Initial situation: the „Sin“
0,6m
Excavation in 600 mm distance from tree stem
How many roots severed?
Diameter of roots affected?
Distance from stem?
Resistance against Uprooting is questionable
Arising questions:

## Slide 23: Symptoms of Reduced Safety
Large growth deficits on the stem
Recessions in the stem
DBH1 = 146, DBH2 = 110 [cm]
Resistance against Fracture of Stem

## Slide 24: Symptoms of Reduced Safety
Ability of compensation
Increase of the root flare diameter results in disproportionately increased breaking safety
110cm
146cm
Factor 2,3
Resistance against Fracture of Stem
Bending resistance moment= D³x π/32
146/110cm=1,33; 1,33³ = 2,34

## Slide 25: Pulling Test Method
Factors for Windload analysis
Wind speed: 32,5m/s
Air temperature: 0° C
Height above sea level: 740 m
Terrain roughness: EN1991: Cat. 3
Crown reaction: Cw 0,25
Exposure: low
Properties of green wood:
Young´s modulus : 8500 MPa
Comp. strength: 20 MPa
Limit of proportionality: 0,24%
Stem diameter: DBH = 146/110 [cm]
Geometry of the stem:
Small leaf Linden, H= 23 m
Gale Moment: Mb = G x cw x /2 x  [ h(z) x A(hz) x v(z)2
18,3 kN
15,4m
Evaluation of Tree Safety

## Slide 26: Results: Factor of Safety of Stem and Root-Soil Compound
Basic Safety 5,0
1,9
1,6
Results of Pulling Test Measurements with ArboStat

## Slide 27
Online Calculation of breaking Safety of the Stem
There is a much easier way!
www.treecalc.com

## Slide 28: TreeCalc does it all
MAC
iPAD iPHONE iPOD
Android
Linux
Windows
Blackberry
Versatility

## Slide 29: Access: www.treecalc.com
Browser based Online Software

## Slide 30: Login
Free Code EZEVL4 / I49JLK (8.3.19)

## Slide 31: Data Entry:
Basic Data

## Slide 32: Data Entry:
Display Geo Position of desired Tree

## Slide 33: Data Entry:
Basic Data
Species related data

## Slide 34: Data Entry
Tree height needs to be measured acurately
Tree Species and Tree Height

## Slide 35: Data Entry
Stem Geometry
146 cm
110 cm

## Slide 36: Data Entry
The wind resistance of tree crowns can either be obtained from a lookup table or be entered individually.
Drag Coefficient of Tree Crown

## Slide 37: Data Entry
Published data of material proper-ties of green wood can be picked from lookup tables.
Individual values can be entered.
Compr. strength of green wood [MPa]
Compressive Strength of Green Wood

## Slide 38: Data Entry
250 kNm
Wind Load
500 kNm
Capacity
Factor of safety 2
Tree
Wind load
Stem diameter
Wood strength
Anchorage of roots
Structural Deficits
Location
Tree height
Wind resistance
Crown area
Dampening effects
Expression of how much stronger a tree is than it needs to be for an intended load
Factor of Safety

## Slide 39: Data Entry
Wind zones acc. to EN 1991-1-4
For each European country individual norms apply.
e.g. Germany has 4 zones
Wind zone | Wind speed | Wind pressure
 | (m/s) | (kN/m²)
1 | 22,5 | 0,32
2 | 25 | 0,39
3 | 27,5 | 0,47
4 | 30 | 0,56
Wind Speed

## Slide 40: Data Entry
10 Basic Crown Shape Patterns

## Slide 41: Data Entry
The Crown shape can be either adjusted with a ruler or by swiping.
To avoid accidental adaption on a small screen the shape can be locked.
Adapting Basic Tree Crown Patterns

## Slide 42: Data Entry
The wind pressure is influended by wind speed and the mass of the air.
The roughness of the terrain´s surface influences the wind speed in the boundary layer.
Trees are often better wind protected in urban settings with multi story buildings.
Wind pressure
Surface Roughness

## Slide 43: Calculate Button
Running a Calculation
Cost: 1 Calc
1,85-2,49 €
8-10,7 Zł

## Slide 44: Results
Basic Safety, Residual Wall, Magnitude of Decay Extent
Basic Safety
Factor of Safety
Required residual wall
Influence of cavities
on stem breaking safety

## Slide 45: Results
Explanations
0,85

## Slide 46: Results
Various stem cross-sections
Adaption to relevant load direction
Adaption of the opening
  Basic safety = colour coded
Legend: > 0
1><1,5
<= 1,5
Stem Geometry

## Slide 47: Results
Different load bearing capacities of varying cross-sections can be compared to stem tomography and evaluated
Stem Geometry

## Slide 48: Results
A new function enables assessment of weak zones in upper regions of tree stems
Shift Height of Damage on Tree Stems

## Slide 49: Results
Shifting height of cross section level
Different load bearing capacities of varying cross-sections can be compared to tomography and evaluated
Shift Height of Damage on Tree Stems

## Slide 50: Results
In case the desired safety margins are not sufficient a crown reduction is being proposed.
Whether a crown reduction is feasible has to be revised.
Statements referring to the magnitude of a crown
reduction are given in meters of tree height or in percent according to German norms.
Crown Reduction
Recommendations

## Slide 51: Reports
Overview of all parameters used
Tree position in map
Results and pics of stem diameter (Tomography)
Report Print Outs

## Slide 52: Reports
Evaluation of the influence of cavities in the upper stem on the tree´s breaking resistance.
Suggestion for crown reduction if the safety factor is below threshold.
Comments can be enterd as well as signature and company stamp
Report Print Outs

## Slide 53: Examples
Oak at Ashton Court, UK

## Slide 54: Examples
Scott´s Pine at Feldafing

## Slide 55: Examples
Damage in different Heights above Ground
0,5 m
8,0 m

## Slide 56: Backend
My Account
Purchasing „Calcs“
History of payment method
History of payments

## Slide 57: Backend
History

## Slide 58: Backend
Report Settings

## Slide 59: Pros over previous versions:
Access at any time at any location with internet access
No software maintenance (e.g. update installation, data backup)
No extra cost for software updates
Fair cost for a „second opinion“
Users trying out different calculations, pay 10-20 € per tree including report
https://treecalc.com

## Slide 60: Pros over previous versions:
Written documentation as pdf reports
All data are being stored in a database and can be exported for further use
https://treecalc.com

## Slide 61: Pros over Cost free SIA Versions:
https://treecalc.com
More crown shapes
Modification of the crown shape
More material properties of different species
Selection of more cross sections
More acurate crown reduction recommendations
All parameters can be modified individually
Shifting height of compromised zone at stem
More transparency, all parameters are presented more comprehensible

## Slide 62: Cons against previous versions:
https://treecalc.com
Pay as you use

## Slide 63: Troubleshooting
Android: disable add blocker software in Firefox.
Rough ruler movement often is slow and unprecise using
Firefox and Android browsers (fastest browser is Chrome)
https://treecalc.com

## Slide 64
Thank You for Your Attention
https://treecalc.com